## Slide 1: Paradox Ethernet/USB Interface Components
Display SSD1306
128X64
LM2598
DC-DC Down Converter
Arduino Mega 2560
Or Compatible e.g. Funduino
Ethernet Shield
W5100
120 Ohm Resistor 0.25W
Paradox Serial Cable

## Slide 2
Arduino MEGA 2560
LM2598
7V DC
OLED
128X64
I2C
Ethernet
Shield
SPI,Vcc
12V DC
Ethernet
UART
UART
Paradox SPxxxx - EVOxx
Paradox Ethernet/USB Interface
5V DC
Vin
Rx1/Tx1
SDA/SCL
5V
USB
Paradox Ethernet/USB Interface Block Diagram

## Slide 3
SDA
SDA
SCL
SCL
5VDC
GND
Arduino
MEGA 2560
Display SSD1306
128X64
Ethernet
Shield
7VDC
GND
12V DC
GND
LM2598
Tx
Rx
Rx1
Tx1
Optional Display
Adjust for 7V DC Output
External DC-DC down converter in use to avoid overheating of Arduino Board Voltage Regulator
LAN
Paradox
Panel
120 Ohm
Wire 120 Ohm Resistor after successful programming.
Only Required for proper USB Operation
USB
Paradox Ethernet/USB Interface Wiring

## Slide 4
Paradox Ethernet/USB Interface
3D-Print Enclosure
Bottom Case
Top Case

## Slide 5: Guidelines
USB Connection to Panel (usb to serial implemented on Paradox Interface) similar function to 307USB.Requires 120-Ohm Resistor between Reset and 5V.
DHCP functionality and OLED display to inform IP address and Serial Settings.
Static IP addressing is recommended.
Up to 3 multiple Connection.
Telnet to Port 23 to show device CLI.
Settings stored to internal EEPROM.
Serial Baud rate is configurable to support SP and EVO series Panels.
OLED Display is optional but recommended , for convenient use , as informs for device IP address and Serial Settings
DC-DC down converter is optional but recommended to avoid over heating Arduino Board regulator.
3D-Print case has been designed to accommodate device.Two versions have been designed with/without OLED 128X64 Display.